## Slide 1
A Simulation-based Approach to Capacity Constrained Mandatory Location Choice Models: An ActivitySim Implementation
June 5, 2023
Innovations in Travel Analysis and Planning Conference
Indianapolis, Indiana
Ali Etezady, David Hensle, Joel Freedman

## Slide 2: Content
Background
New approach
Implementation & results
Conclusion

## Slide 3
Background

## Slide 4: Background
Mandatory location choice models are integral parts of Activity-based models and are also increasingly common in trip and tour-based models.
  They determine the workplace or school location of individuals in the model.
These models are often formulated using the logit family of random utility models.
  Advantages: flexibility in defining the factors affecting choice, efficiency of the method, and the general availability of estimation software packages
  Disadvantage: (in general) inability to doubly constrain the model in the estimation process, requiring an iterative post-estimation process to match input attractions

## Slide 5: Background: the need to doubly constrain choice models
A location choice model by design ensures matching the origin constraints.
  The sum of the number of workers with assigned workplace matches the total number of workers
But it does not ensure matching the destination constraints
  No guarantee the number of assigned workers to a destination zone matches available jobs there.
Origin constraint:
(given, since
)
Destination constraint:

## Slide 6
Background: solution
Solution 1: estimate constrained location choice models
  Hard to solve and expensive to run [1]
  Not guaranteed to match input attractions in implementation
Solution 2: constrain the model after estimation.
  Use shadow pricing: an iterative process in which constants are added to the utility of each destination alternative and adjusted so that the model output matches the destination constraints
  [1] Bernardin, V., S. Trevino, G. Slater & J. Gliebe. “Simultaneous Travel Model Estimation from Survey Data and Traffic Counts.”

## Slide 7
Calculation of shadow prices
Shadow prices are usually calculated in one of two ways
  Additional alternative-specific constant for each destination zone
where:
Sample Utility Equation:
Uj = βlogsum * logsumij + βdist * distij
+ ln(retail_empj + θservice_emp * service_empj)
+
(quality variables)
(quantity variable - size)
(shadow price)
(requires iteration)

## Slide 8
Calculation of shadow prices
Shadow prices are calculated in one of two ways
  Additional alternative-specific constant for each destination zone
  Multiplier on size term
where:
Sample Utility Equation:
Uj = βlogsum * logsumij + βdist * distij
+ ln(retail_empj + θservice_emp * service_empj)
*
(quality variables)
(quantity variable - size)
(shadow price)
(requires iteration)

## Slide 9: Purpose and need
Shadow pricing is slow
Most activity-based models use a process called ‘shadow pricing’ to ensure that total workers who choose to work in a zone is proportional to the total input employment in the zone
The models do this by running the work location choice model, comparing total workers to total input employment, and calculating a ‘shadow price’, or zonal adjustment factor, to use in the next iteration.
The process is repeated until the model ‘converges’.
This is a slow process.

## Slide 10: Purpose and need
Shadow pricing is not guaranteed to converge
Because of the way that the prices are calculated (by segment), there’s no guarantee that total workers will equal total input employment after any number of iterations.
The procedure does not consider in-commuting or out-commuting, which can be problematic for regions with big neighbors.

## Slide 11: Purpose and need
Managing shadow prices is a pain
There are no definitive rules for when this process should be run, and when it can be turned off to save runtime.
If shadow pricing is turned off, some other version of shadow prices is typically used as an input. But its not clear which prices should be used or how good they are.
Shadow prices also don’t work very well with small sample sizes.

## Slide 12
Simulation Approach

## Slide 13: Revised constraint mechanism
We created a new simulation-based constraint mechanism in ActivitySim that greatly speeds up runtime and accuracy
Runs all workers through location choice
For each zone, compare estimated workers to total input employment. If zone is over-estimated, randomly select workers (equal to the number over the total jobs) and re-run them in the next iteration after removing all over-estimated zones.
The new procedure is much faster than shadow pricing and is guaranteed to converge. And no more shadow prices to manage.

## Slide 14: Revised Approach
Run model with all workers_to_simulate
Calculate Cj each zone
Cj < 1
Set workers_to_simulate = ALL
Set Shadow_pricej = -999
Set nj = extra number /share of workers from zone j
Set Shadow_pricej = 0
Set nj = 0
All Cj = 1+ tol
Yes
No
Quit
Sample nj from each zone
Set workers_to_simulate = n = union(nj)

## Slide 15
Implementation

## Slide 16: Implementation
The simulation-based method was implemented within the ActivitySim framework, an open-source activity-based travel demand modeling platform.
  Capacity constraint method can be set in the model’s shadow pricing settings file.
Previously, ActivitySim had the option of the usual shadow pricing methods (multiplier on size term or additive constant).
  These options can be turned on for workplace location or school location choice models.
  Target data (zonal employment or enrollment come form the land use data).

## Slide 17
Testing & results

## Slide 18: We Use the SEMCOG model for testing
(Southeast Michigan Council of Government) SEMCOG model:
  1.9m households
  4.7m persons
  28600 zones (microzone)
Workplace location model tested
  Convergence criteria:
    Modeled size (share of workers in MAZ) within 5% of desired size (share of employment in MAZ)
    Maximum of 1% of zones allowed to fail to meet above target

## Slide 19: Workplace location choice constraining: convergence
Chart: Change in workers to simulate size in each iteration
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10

 | 1 | 0.14056 | 0.055591 | 0.021552 | 0.0089446 | 0.0058153 | 0.0040688 | 0.0037528 | 0.0032102 | 0.0030732

## Slide 20: Percent of MAZs not reaching convergence
Note: convergence for legacy method is based on proportion of workers in MAZ compared to proportion of size term in MAZ
There are four size term segments (by income group) so if any of the four fail to reach convergence, MAZ is flagged as failing for shadow pricing method
Chart: Convergence (achieved if %failed zones < 1)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Simulation-based method | 0.50766 | 0.21786 | 0.082655 | 0.040472 | 0.021965 | 0.015574 | 0.011908 | 0.010301 | 0.0094284
Legacy method | 0.42333 | 0.40605 | 0.40573 | 0.40556 | 0.40566 | 0.40416 | 0.40612 | 0.40577 | 0.40538 | 0.4043

## Slide 21: Testing: model worker vs. land-use employment
iter1
iter2
iter3
iter4
iter5
iter6
iter7
iter8

## Slide 22: Testing: Run time
10 iteration run (Simulation-based method runs for 9 iterations as it converges)
Chart: Workplace location model run time
| Simulation-based method | Legacy method
 | 49.5 | 300.3
16 intel cores
150 GB of RAM

## Slide 23: Revised shadow pricing: average half-tour length change
Chart: Average home-work distance (miles)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Legacy methods | 12.65 | 12.75 | 12.82 | 12.85 | 12.87 | 12.89 | 12.9 | 12.89 | 12.88 | 12.89
Simulation-based method | 12.65 | 12.72 | 12.78 | 12.84 | 12.84 | 12.86 | 12.86 | 12.86 | 12.86

## Slide 24
Conclusion

## Slide 25: Conclusion
Common location (destination) choice models are not capacity constrained by design.
Current model constraint mechanism are inefficient and time-consuming to run in real-world applications.
Our tests show the simulation-based approach not only runs significantly faster, but also converges faster than the legacy methods.
Method currently implemented for SEMCOG (Southeast Michigan) and SANDAG (San Diego) ActivitySim-based models.

## Slide 26: Acknowledgement
This work was funded by the ActivitySim Consortium.
We would also like to thank the Consortium, SEMCOG, and SANDAG teams for their feedback in developing and implementing this approach.

## Slide 27
Joel Freedman
Senior Director
Joel.Freedman@rsginc.com
Ali Etezady
Consultant
Ali.Etezady@rsginc.com
David Hensle
Consultant
David.Hensle@rsginc.com